## Slide 1: How To Train Your Borg
May 19, 2012
Lloyd Moore, President/Owner
Just kidding – next slide please!

## Slide 2: Robothon Line Following Algorithm
May 19, 2012
Lloyd Moore, President/Owner

## Slide 3: Agenda
Rules review
Objects and Behaviors
Left hand rule, right hand rule
Remembering a path
Simplifying a path
Replaying a path
Software design and implementation
Note: This presentation is based on previous work from Richard T. Vannoy II and is compatible with that presentation.

## Slide 4: Line Maze Key Rules
See http://www.robothon.org/robothon/maze.php for complete rules!!!
“Track” is a ¼” black line on white background
Starting point marked with a “T”, ending point marked with a 6” circle
Dead ends not marked, line simply terminates
No loops!
All intersections are at right angles
3 Attempts to solve the maze, and can remember it
3 minute time limit for each run

## Slide 5: Objects In Maze
Rules of the maze determine what objects we need to watch for in the maze:
  Start Marker
  Stop Marker
  Line or Maze Path
  Dead End
  Turns
  Intersections
    “T” intersection
    4-Way intersection
    Straight or Left Intersection
    Straight or Right Intersection
Goal of our program is to detect these objects while the robot runs the maze and make take the correct action in each case

## Slide 6: Detecting Object Types
Each object type will show up as a different pattern on the reflective sensor
Sensors are analog and increase in value as more black appears, will basically want each sensor centered over one edge of the line.
Key is to look at BOTH sensors to make decisions
Some objects may appear similar on single scans, but keeping a history of prior readings can help sort this out (2-3 should be enough)
Once you know the object type you have for a particular point in time you can give it a name/symbol and use that to simplify making a decision, can also store these symbols in memory to remember / manipulate a path

## Slide 7: Behavior for Each Object
For each movement interval the robot needs to decide what action to take for the next movement interval.
Fixed number of objects we know about, so fixed number of actions:
  Start Marker –> Treat as dead end
  Stop Marker –> Stop, you have completed the maze
  Line or Maze Path -> Go straight, make centering corrections
  Dead End -> Turn around and go back
  Turns -> Follow the direction of the turn and re-center
    For the most part these can be ignored, just follow the line
  Intersections -> Pick a direction to explore and store it, execute a turn
    “T” intersection
    4-Way intersection
    Straight or Left Intersection
    Straight or Right Intersection

## Slide 8: Left Hand Rule
Comes from formal graph theory, but don’t need to worry about details here…. (Rumor has it this was the discovery that made PacMan possible!)
States that when given a 3 way choice over which way to go if you choose left first, then straight, then right you are GUARANTEED to cover the whole maze!

## Slide 9: Right Hand Rule
Fundamentally the same as the Left Hand Rule
Just pick one and stick with it!

## Slide 10: Remembering A Path
Basically remembering which action/behavior you took at each intersection
Only need to remember turns as those are the only points where you have choices
Basic choices are:
  Straight
  Right
  Left
  U – turn, helpful for simplifying mazes

## Slide 11: Remembering a Path
Path is just a series of turns!
Don’t need to worry about distances between turns at this point as we don’t have any loops in the maze!
We set up symbols for each decision (S,U,L,R)
Just store these in a string or memory buffer:
  “SRRULR”
Now you can replay and manipulate the path when you start from the same point and use the memory buffer to select which behavior / action to take at each decision point!

## Slide 12: Simplifying a Path
Basically amounts to removing “backtracking” in the stored path.
Remember we have NO LOOPS in the maze
Because of this each instance of “backtracking” will be marked by a dead end or “U” symbol in the path
Typical path stored in memory: “….RSUL”
If you draw this out graphically “SUL” really means we went right at the last turn so replace “SUL” with “R” to simplify the path giving: “….RR” from the original path
Need to do this for all combinations

## Slide 13: Replaying a Path
Fundamental concept here is to replace the Left / Right hand rule for deciding which path to take with recall from an optimized path
Instead of having to explore to find out if the end of the maze results from a given turn (exploration) it can simply recall the best known decision from memory (recall)

## Slide 14: Software Design
General operation
  Put bot down and start it
  Bot runs around maze until either 3 minute time out happens or the end of the maze is found
  During operation the bot has to determine which object it is looking at, then determine which behavior to use
Two key modes of operation
  Exploration
  Recall
  Key difference is the mechanism used to map objects to behaviors
These two block will form the basic structure of the program!
Discussion and slides here designed to be compatible with this presentation.

## Slide 15: Enhancements
Many enhancements that can be made once the basic program is working
  More advanced path optimization, note since we have no loops currently only one solution will exist!
  Ensure no movement delays from processing (should indicate a bug since processor is reasonably fast)
More line sensors for better control, and deeper processing of the analog signals
“Light skirt” to block stray light from coming in
Add encoders to measure distance, speed up on straight segments

## Slide 16: Summary
Reviewed the rules for the Line Maze
Determined the objects and behaviors
Left/Right hand rule
Paths: Remembering, Simplifying, Playback
Software design
Enhancements to get better times!

## Slide 17: References
Robothon Online Rules: http://www.robothon.org/robothon/maze.php
Others:
  http://en.wikipedia.org/wiki/Maze_solving_algorithm
  http://www.pololu.com/file/0J195/line-maze-algorithm.pdf